## Slide 1: PhD pitch of DC3 Amirhossein Hassani
AI for Road Safety in LMICs
IVORY Consortium Meeting and Training Event
Athens, 14-15 April 2026

## Slide 2
Automatic Attribute Detection for Imbalanced Datasets
EfficientNet-Swin Transformer for automated iRAP road safety attribute extraction in low- and middle-income countries. International Congress on Transportation Research 2025 (ICTR 2025). available online: DOI: 10.5281/zenodo.18822033

## Slide 3
Chart: Single-Frame vs Multi-Frame, Per Attribute M-F1 Score Bosnia Dataset Improving the previous state of the art
| Lane width | Quality of curve | Median Type | Road condition | Vehicle parking | Roadworks | Sight distance | Delineation | Street lighting | Roadside severity - driver-side dist. | Roadside severity - driver-side obj. | Roadside severity - pass.-side dist. | Roadside severity - pass.-side obj. | Paved shoulder - driver-side | Paved shoulder - passenger-side | Property access points | Land use - driver-side | Land use - passenger-side | Sidewalk - driver-side | Sidewalk - passenger-side | Bicycle facility
LSTM CE (%) | 71.21 | 65.99 | 44.45 | 73.32 | 60.57 | 74.29 | 70.85 | 99.17 | 91.38 | 57.05 | 35.26 | 56.87 | 50.51 | 64.71 | 48.52 | 57.28 | 64.46 | 67.08 | 46.08 | 45.83 | 100
LSTM CE-MT-R (%) | 75.6 | 71.24 | 55.62 | 77.7 | 60.28 | 78.8 | 75.67 | 98.94 | 91.53 | 57.86 | 43.31 | 59.97 | 51.06 | 65.02 | 54.01 | 59.71 | 63.85 | 69.6 | 43.72 | 50.19 | 100
ours (%) | 74.66 | 68.63 | 57.1 | 68.71 | 65.04 | 88.86 | 74.96 | 98.66 | 92.26 | 61.6 | 62.05 | 64.65 | 69.44 | 64.27 | 52.33 | 55.69 | 54.54 | 69.27 | 59.83 | 55.84 | 100
20-Frame Model | Red
20-Frame Model with Customized Loss | Orange
Our 1-Frame model | Green

## Slide 4
Related work: Auditing modelled road safety risk
Auditing iRAP’s ViDA risk engine: A two-stage surrogate learning and orthogonalized heterogeneity framework for modelled road safety. Infrastructures, 11(4), Article 129. Available online: 10.3390/infrastructures11040129
The paper studies the modelled fatal-and-serious-injury risk surface produced by the ViDA risk engine and analyses 147,466 road segments of 100 m each from 12 surveys, grouped into four reporting groups. It uses a two-stage framework combining surrogate modelling, explainability, and treatment-level heterogeneity analysis.
It also shows how infrastructure-related attributes can be used in data-driven models to analyze modelled road risk and inform infrastructure improvement priorities.

## Slide 5
Kenya pilot attribute: severe imbalance within a single sidewalk label set Submitted into IRTAD Conference
Passenger-side sidewalk labels already show the long-tail structure that motivates targeted synthesis.
Pilot attribute and label meanings
Target rare class
1 = sidewalk with barrier
Reference class
4 = sidewalk 0m to <1m from road
Other dominant labels
5 = none, 7 = informal path 0m to <1m
Conference pilot
one dataset, one attribute, one rare class
Counts used for the pilot story
Class 1 total
20 images
Class 1 train / holdout
16 / 4
Class 4 reference subset
24 images
Practical meaning
the target concept is genuinely low-resource
Kenya passenger-side sidewalk distribution
Class 1 is tiny; class 4 is a sidewalk reference class, not the head label. The pilot therefore tests a truly low-shot barrier concept.

## Slide 6
Initial result: the barrier concept becomes visible only after adaptation
The rare prompt alone remains visually close to the reference condition; the LoRA introduces the missing concept.
Group A
Reference sidewalk prompt only
Group B
Rare-class prompt only
Observed in pilot: A and B look broadly similar
Group C
Same rare-class prompt + LoRA
Observed in pilot: visible barriers appear in this condition
Core observation
The prompt-only rare-class condition (B) did not reliably separate itself from the reference condition (A). When the rare-class LoRA was added (C), barrier structures became visibly more explicit.

## Slide 7: Thank you for listening!